A Dynamic Hardware Architecture for Future Networks
Master Thesis by Richard Huber
1st Intermediate Presentation
Advisor: Ariane Keller
Co-Advisors: Dr. Stephan Neuhaus, Daniel Borkmann
Professor: Prof. Dr. Bernhard Plattner
[Speaker Notes: /Users/richardhuber/ma/repos/ma/documents/presentations/intermediate1/intermediate1.odp]

---
Outline
- Introduction
- Goal of this Thesis
- Task List
- First Results
- Challenges
- Summary

---
The Autonomous Network Architecture (ANA)
- Abstraction model and framework for interconnecting network protocol implementations.
- Design goals of ANA:
  - scalability
    - adding more functionality
    - different ways of integrating functionality
  - adaptability
    - changes in the network environment
    - changes in the traffic pattern
    - changes in the node platform
- LANA: Software prototype implementation

---
The Autonomous Network Architecture (ANA)
Strongly layered architecture of the current internet
Adaptable architecture of ANA, functional blocks can be interconnected on demand

---
ReconOS
- Heterogeneous multi-core architecture
- Reconfigurable hardware threads execute tasks on behalf of the CPU

---
Hardware Support for ANA
- Use ReconOS to extend LANA with hardware support
- Execute functional blocks in hardware threads if they require
  - high computational performance
  - low latency

---
The Processor Local Bus (PLB)
- ReconOS uses a shared bus (PLB) to exchange data
  - from HW threads to SW
  - from SW to HW threads
  - between HW threads
- With ANA as use case, PLB is the bottleneck of ReconOS.

---
Goal of this Thesis
- Extend the ReconOS architecture
- Provide an infrastructure for high throughput data transfer
  - between HW threads
  - between SW and HW threads
- Provide an interface for configuring hardware networking blocks from software

---
Task List
- Familiarization
- Evaluation of possible architectures
Communication between HW blocks
- Configuration interface
- Communication between HW blocks and SW
- Performance evaluation

---
Evaluation of possible Architectures
- Single Bus
  - Throughput does not scale
- Multibus
  - Length and capacity of interconnecting wires do not scale
- Peer to Peer
  - Chip area utilization and wire length do not scale
- Network on Chip (NoC)
  - Good trade-of between performance and resource utilization

---
Evaluation of NoC Topologies
Functional Block
Switch
- Grid Topology
- Ring Topology
- Extended Ring Topology

---
Worst-Case Link Load
- Calculate worst-case load for the individual links
- Sum up the worst-case loads of all links to a total required capacity
Number of Nodes
Total Required Capacity

---
Extended Ring Topology
- Good trade-off between routing complexity and required link capacities
- Adaptable to any number of nodes

---
Task List
- Familiarization
- Evaluation of possible architectures
Communication between HW blocks
- Configuration interface
- Communication between HW blocks and SW
- Performance evaluation

---
Challenges
- High testing and verification effort (typical for VLSI development)
- Usability seems not to be the VLSI tool vendor's design principle

---
Summary
- Use ReconOS for ANA implementation
- Global bus used by ReconOS is system bottleneck
- Develop NoC for interconnection of HW threads
- Extended ring topology is a good trade of between hardware resource utilization and performance