# Generic algorithm to determine the worst-case link utilization
## Scenario
Data sources and sinks: All functional blocks are allowed to produce and consume data at line rate (1Gbit/s).
Switching blocks: All switching blocks are connected to one specific functional block.
Routing: Only static routing considered, routing tables are determined by the network topology, no load ballancing.
## Algorithm
1. Set up network as a directed graph GNET=(V,E) with
  1. V the set of all nodes v,
  2. E the set of all links e=(vi,vj) able to forward packets from node vi to vj.
2. Let EOUT, i be the set of negative incident edges of node vi.
3. For all nodes vi in V select a routing policy Ri: vDEST → eOUT where vDEST ≠vi is the destination of the routed packet and e_out in E_{OUT,i} is the outgoing link chosen to forward the packet.
4. Send packets to determine the possible network utilization
  1. All nodes v_SRC in V send exactly one packet p=(vSRC, vDEST) to all other nodes v_DEST in V, v_SRC neq v_DEST
  2. All links ei in E refer to a bipartide graph GLINK,i=(Si,Di,Li). Si, Di and Li are initialized as empty sets. Upon forwarding packet p=(vSRC, vDEST) over the link ei, the link
    1. Adds vSRC to Si (if v_SRC notin S_i )
    2. Adds vDEST to Di (if v_DEST notin D_i )
    3. Adds the edge (vSRC,vDEST) to Li.
5. Select worst-case scenario for every link ei
  1. With the bipartide graph GLINK,i=(Si,Di,Li) build a maximum matching Mi using the Hopcroft-Karp algorithm.
  2. The number of edges |M| in the matching M is the maximum possible load applied to the link ei in the worst-case.